###### Waves and Sound											Name: ____________________

Simple Harmonic Motion

period, T:										frequency, f: #

wall				  equilibrium position

frictionless floor

period of a mass-spring system:

m = mass (kg)

k = spring constant (N/m)

EX.		A 5.5 kg cat is attached to a fixed horizontal spring of stiffness 22.8 N/m

and is set in motion on a frictionless surface. Find the period of motion of…

…the cat.

…a 240 g mouse, with the same spring and surface.

What stiffness must a spring have so that the period of the mouse’s motion is the

same as that of the cat?

EX.		A 1275 kg car carries two passengers with a combined mass of 153 kg. The

car has four shock absorbers, each with a spring constant of 2.0 x 104 N/m.

Find the frequency of the vehicle’s motion after it hits a pothole.

restoring force:

simple harmonic motion (SHM):

For a mass-spring system, Hooke’s law applies:

energy:

kinetic energy, KE: energy of mass m having velocity v

m (kg); v (m/s)

potential energy, PE: stored energy

For a spring with spring constant k and “stretch” x:

k (N/m); x (m)

For a mass m at a height h above a reference line:

m (kg); h (m); g = 9.81 m/s2

amplitude, A: maximum displacement from equilibrium

frictionless

Energy of a Mass-Spring System

Energy (J)

- The Pendulum

For < 15o, a simple pendulum

approximates SHM.

Energy of a Simple Pendulum

Energy (J)

period of a simple pendulum:

EX.		The period of a pendulum is 5.2 s. Find…

A. …its length

B. …the mass of the bob

period of a mass-spring system

In a simple harmonic motion:

The body of a 1275 kg car is supported  on a frame by four springs. Two riders mass is 153 kg. The frame vibrates with a period of 0.840 s

A. …its spring constant

Waves 	  (    vibrations moving through space and time

medium: the matter through which the energy of mechanical waves moves

transverse waves: particles of medium move

to direction of wave travel

For a transverse wave:

longitudinal (compressional) wave: particles of medium

move       to direction of wave travel

pulse wave:

periodic wave:

- Wave Reflection

fixed boundary									free boundary

- Wave Interference	Two waves (unlike two objects) can occupy the same place at

the same time. This condition is called interference.

constructive interference: 					destructive interference:

- Wave Velocity				Equation:

v (m/s);  (m); T (s); f (Hz)

EX.		A water wave of wavelength 8.5 m washes past a boat at

anchor every 4.75 seconds. Find the wave’s velocity.

The velocity of any mechanical wave depends only on

properties of medium through which it travels.

e.g.,

An empirical equation for the velocity of sound in air:

Standing Waves 		(   incident and reflected waves interfere so that antinodes have a

max. amplitude, while nodes have zero amplitude

On a string, nodes remain motionless; antinodes go from max. (+) to max. (–) displacement.

wavelength of nth harmonic on a string:

EX.		Waves travel along a 96.1 cm guitar string at 492 m/s.

Find the fundamental frequency of the string.

Find the frequency of the 5th harmonic.

frequency of the nth harmonic:

- Standing Waves in Open Tubes

wavelength of nth harmonic of an open tube:

- Closed Tubes

wavelength of nth harmonic of a closed tube:

EX.		Find the fundamental frequency for an open tube of length 1.24 m. Assume the air

temperature to be 20.0oC.

EX.		Find fundamental frequency for a closed tube of length 1.24 m. Air temp. is 20.0oC.

doubling (or halving) of frequency =

100 Hz				200 Hz				400 Hz				800 Hz