###### Circular Motion and Gravity							Name: _______________________

axis: line about which circular motion occurs

rotation:

revolution:



radian: 	the angle subtended by an arc

that is the same length as the

circle’s radius

EX.											If arc subtended by basket between loadings is

3.8 m, find angular displacement, in rad.

Through what arc length does bear move, between stops?

If Ferris wheel rotates at constant angular speed, it takes 18 s to go around once.

Find avg. angular velocity.

In linear kinematics…	 				In angular kinematics…

Ferris wheel takes 2.2 s to go from rest to its avg. ang. vel. Find its ang. acceleration.

In linear kinematics…	 				In angular kinematics…

Find ang. vel. of Earth…

...spinning on its axis.

...revolving around Sun.

Angular Kinematics					Linear Kinematics

EX.		Car wheel initially rotates at 52 rad/s. After braking 7.3 s, wheel is at rest. Find…

a. …wheel’s avg. ang. accel.

b. …wheel’s ang. displ.

EX.		Find ang. accel. of Earth…	…spinning on its axis.

…revolving around Sun.

EX.		Bike wheel w/outer radius 36 cm has init. ang. vel. 5.2 rad/s.

Wheel’s vel. increases to 9.8 rad/s. Ang. accel. is 0.68 rad/s2.

a. How much time elapses?

b. Find ang. displ. over this time.

c. Wheel goes around how many times?

d. What linear distance is covered?

period, T: time (in s) to go around once

frequency, f: # of cycles in one second (Hz)

Since   , then…							   and…

tangential acceleration:

EX.		Bike wheel spinning initially at 5.8 rad/s speeds up to 9.3 rad/s

over 15 s. Find tang. accel. for reflector and valve stem.

(rstem = 41 cm; rreflector = 32 cm)

valve stem…

reflector…

Find tang. speed after 15 s for both valve stem and reflector.

valve stem…

reflector…

EX.		Earth-Sun distance is 1.5 x 1011 m. Find Earth’s lin. speed around Sun, in m/s.

EX.		Normal, IL is at 40.5o N latitude. Find tang. speed of Normal

around Earth’s axis. Earth’s radius is 6.38 x 106 m.

centripetal acceleration (ac): acceleration toward the center

For circular motion, tangential acceleration (at)

may be zero or nonzero…

(i.e., when  = 0)

...but

EX.		Earth-Moon distance is 3.84 x 108 m.

a. Find tangential and centripetal accel’s of Moon around Earth.

b. Find resultant (or net) accel. of Moon.

at and ac are      component vectors of the net accel.

c. Find tang. vel. of Moon around Earth.

d. With what force does Earth pull on Moon? Mass of Moon is 7.36 x 1022 kg.

Recall Newton’s 2nd Law: 	F = m a

centripetal force:

EX. 	2.6 kg stone at end of 0.74 m rope is whirled in horiz.

circle at constant rate. Period is 1.1 s. Find rope’s tension.

EX.		At bottom of circular loop of radius 16 m, roller coaster car

(m = 250 kg) travels at 13 m/s. Find force of track on car.

Centrifugal “Force”		--

--

--

Consider an amusement park ride:

EX.		Student (m = 55 kg) rides bus moving 15 m/s around curve of

radius 16 m. Student is pressed against window. Find centrifugal

“force” student senses.

EX. 		Space station, radius 8.0 m. At what rate must station spin so

occupants feel Earth’s gravity?

force on person			Earth’s gravity

Find g at eye level, if avg. person height is 1.7 m.

Gravity

Brahe:

Kepler:

Kepler’s Laws…

1.

2.

3.

EX.		Earth is 1.50 x 1011 m from Sun; Jupiter is 7.78 x 1011 m.

How long does it take Jupiter to go once around Sun?

Newton:

Cavendish:

45 kg girl and 53 kg boy are 14 m

apart at jr. high dance. Find force of

gravity acting to bring them together.

EX.		Earth has mass 5.97 x 1024 kg and radius 6.38 x 106 m. Find

force of gravity on 34.0 kg rock.

For any object of mass m and mean radius r:

EX.		Mars has radius 3.40 x 106 m. If a 12.0 kg rover weighs

44.5 N on Mars, find mass of Mars.

What is g on Mars?

Gravitational field

-- arrow direction shows how a dropped object would accelerate

--

Einstein’s Idea of Gravity: The General Theory of Relativity

Masses don’t attract other masses via gravity. Masses (especially, large ones) alter the “curvature” of space (and time) around them. The paths of nearby objects are then affected by this curvature of space. Thus, a dropped pencil falls – NOT because there is a force between its mass and that of the Earth – but because the space around the Earth is “curved” in a particular direction (i.e., downward) and the pencil must follow the curvature of space.

# Text boxes

A spinning circle of

radius r…

r

r

1 rad

Conventions for

, , and ...

r



vt

at



r

Normal

axis

equator

6.38 x 106 m

vt



r

ac

at

ac

ar

axis of

motion

object

at

ac

Add like any two     vectors.

ac, Fc

vt



r

m

r

axis

you

(aerial view)

axis

axis

FROM YOUR FRAME

OF REFERENCE

FROM A BIRD’S FRAME

OF REFERENCE

axis

Every object in the universe attracts every other object by gravity.

m = objects’ masses (kg)

r = separation between objects’ centers of mass (m)

G =

m2

m1

r

SUN

r = 11.5 m

r = 7.5 m

Ferris wheel